# Module 4 Demo 4: Application Profiling Using Sun Studio
This exercise demonstrates the use of the complementary profiling capabilities of the NetBeans profiler and the Sun Studio Collector Analyzer.
### Required Software
- Solaris OS (Sparc or X86)
- Java 6 JDK or higher
Sun Studio version 11 or 12
You can download Sun Studio from http://developers.sun.com/sunstudio/downloads/.
Java2Demo
Located in: <JDK install dir>/demo/jfc/Java2D/Java2Demo.jar
### Objective
Use the NetBeans profiler and the Sun Studio Collector and Analyzer tools to profile Java technology applications.
### Preparations
Check for required version of Java SE.
Use the java -version command to check the installed Java SE version.
If the installed version is earlier than Java SE 6, download and install the latest Java SE version from the following URL.
http://java.sun.com/javase/downloads/index.jsp
Download and install Sun Studio.
Download and and install Sun Studio from the following URL:
 http://developers.sun.com/sunstudio/downloads/
Add the bin subdirectory of the Sun Studio install directory to the Solaris OS PATH variable. For example, if you installed Sun Studio in the default location /opt/SUNWspro you can enter the following commands at a terminal window.
PATH=/opt/SUNWspro/bin:$PATH
export PATH
Download and install NetBeans 6.1.
Download and and install NetBeans from the following URL:
 http://www.netbeans.org
Add the bin subdirectory of the NetBeans 6.1 install directory to the OS PATH variable.
### Instructions
Profiling using the NetBeans profiler.
Start the NetBeans IDE using the NetBeans desktop icon by entering the following command in a command line window.
netbeans
1. In NetBeans IDE, select Profile > Attach Profiler menu option. Click on the CPU icon on the left. Select to profile Entire Application on the right. Leave the default filter as Profile all classes and click on Attach. Select Application as the target type of profiling. Select Attach Method of local and Attach invocation of Dynamic. Finally, select Java SE 6.0 as the Java platform to run your application to complete the wizard interaction.
2. When the Select Process dialog is displayed in NetBeans IDE, use a command line window and launch the Java2Demo application with the follwing command line options.
java -server -Xmx15m -Xms15m -Xmn3m -XX:+UseSerialGC
-jar <JDK install dir>/demo/jfc/Java2D/Java2Demo
1. On NetBeans IDE, press the Refresh button in the Select Process dialog and press OK.
2. NetBeans will instrument the running Java2Demo.
3. Click on the Live Results icon in NetBeans IDE in the left panel Profiling Results. When NetBeans has finished instrumenting the Java2Demo application, it will start displaying live profiling results.
4. Now click on the Transforms tab of the Java2Demo application.
5. You can now observe the Java level methods which are consuming the most time in the application in NetBeans IDE.
The NetBeans Profiler should show that approximately 45% of its time is spent in java2d.AnimatingSurface.run method.
Profiling using the Sun Studio Collector and Analyzer tools
Open a command line window and change to exercises/mod04/working directory
cd exercises/mod04/working
Run Java2Demo using the following command line.
collect -j on java -server -Xmx15m -Xms15m -Xmn3m -XX:+UseSerialGC -jar <JDK install dir>/demo/jfc/Java2D/Java2Demo
This invokes the Sun Studio Collector to capture a running profile of the Java program. It creates a file in the current directory called test.er.1.
The default sampling interval is 1 second and the default output directory is the present working directory. Please refer to the Sun Studio Collector documentation for command line options that override default values.
1. After the Java2Demo is launched, click on the Transforms tab and leave the Java2Demo run for about 15 or 20 seconds. Then, quit the Java2Demo program.
2. Now use the Sun Studio Analyzer to open the test.er.1 experiment just collected.
  analyzer test.er.1

### Analysis
This section compares and contrasts what was seen in Collector / Analyzer with what is seen in NetBeans Profiler.
The NetBeans Profiler showed that approximately 45% of its time was spent in java2d.AnimatingSurface.run method. However, it is very hard to find that method in the Collector / Analyzer profile.
If you examine the source code for java2d.AnimatingSource.run method, (viewable at
<jdk install dir>/demo/jfc/Java2D/src/java2d/AnimatingSurface.java) you will see that there is not much to the run method. That is because much of what was seen in Collector / Analyzer <JVM-System> is what is executing within the body of java2d.AnimatingSource.run method.
This example illustrates how the two profilers can compliment each other. The NetBeans Profiler shows much of the time is spent in java2d.AnimatingSource.run method which might not say much about what is really going on inside of that method. You need to look at, or re-look at the Collector / Analyzer profile to get a better idea of what's happening within java2d.AnimatingSource.run method.
If you considered the task under way was to identify performance tuning opportunities with the Java2Demo, the view in Sun Studio Analyzer does not provide much help if you want to focus on Java level optimization opportunities. It appears that in the default view the majority of the time is spent within <JVM-System>. Changing the User Mode in the Set Data Presentation dialog to Expert or Machine shows the JVM methods where the time is being spent. This is great for JVM developers. But, not much benefit for a developer wanting to improve the performance of Java2Demo at the Java code level.
NOTE: For server side applications, especially those that run an extended period of time, using Collector / Analyzer works very well at identifying performance optimization opportunities. It is these same class of applications that are more difficult to setup, configure and profile with traditional Java profilers such as NetBeans Profiler.